## Slide 1: Assistive Robotics Part 2

## Slide 2: Agenda
Recap of Assistive Robotics Part 1
Human muscles and signals
Muscle activation as an input
Workshop Project

## Slide 3: Recap of Assistive Robotics Part 1
Let’s run it back!

## Slide 4: Simple motor control
Make the motor rotate from max angle to min angle only on button press
rasr-lab.github.io/education/
Button_servo_control.py
Activity:

## Slide 5: Human muscles and Signals
What makes us move!

## Slide 6: Structure of a muscle
Soft tissue
Muscle fibers bundled together
Blood supply within the muscles
Tendons connect to bones

## Slide 7: Structure of a muscle
Muscles need electrical activity to contract
Nerves supply electrical stimuli
Human nervous system generates electrical stimuli based on intent

## Slide 8: Sensing Muscle Activity
This “electrical stimuli ” can me measured
The tool is called an Electromyograph
  Needle EMG
  Fine-wire EMG
  Surface EMG

## Slide 9: Let’s see an EMG sensor in action!

## Slide 10: Muscle Activation As An Input

## Slide 12
Time (s)
Muscle Activity (%)
Muscle Activated
Muscle Not Activated
Threshold
0
100

## Slide 13: The sensor we will use is
Can be connected to the microcontroller
Cheap and convenient
Readily available
Already provides an Envelope Signal

## Slide 14: The sensor we will use is
Red: +5V or Vin
Black/Green: 0V or GND
White: ENV (Envelope)
Let’s attach the sensor to our biceps

## Slide 15: Blink the onboard LED
Use the EMG sensor to turn the LED on/off
rasr-lab.github.io/education/
Blink_LED_EMG.py
Activity:
+5V
GND

## Slide 16: Blink the onboard LED
Use the EMG sensor to turn the LED on/off (with a filter)
rasr-lab.github.io/education/
Blink_LED_EMG_
filtered.py
Activity:
+5V
GND

## Slide 17: Workshop Project

## Slide 18: Workshop Project
Control an exoskeleton using your muscles
  Connect the exoskeleton to a microcontroller
  Attach the exoskeleton to the doll
  Use your muscle to move the exoskeleton
  The motor returns to original position once the input goes away

## Slide 19: Control the Servo with your muscle
Use the EMG sensor to turn the LED on/off (with a filter)
rasr-lab.github.io/education/
Exoskeleton_EMG_Servo.py
Activity:
+5V
GND

## Slide 20: Attach the Exoskeleton to the Doll
Make sure the Exoskeleton lines up with the elbow joint
Use masking tape to attach the Exoskeleton to the doll
Activity:
Make the dolls elbow flex/extend using the Exoskeleton

## Slide 21: What else can you do with this setup?

## Slide 22: Thank you!
Sandesh G. Bhat
Assistive Systems and Robotics Engineering
bhatsg@uwec.edu